## Slide 1
Ambulance Safety For Children
A Perspective and a Goal
NASEMSO
Safe Transport of Children Committee
Washington, DC
April 6, 2016
Marilyn J. Bull, MD, FAAP
Morris Green Professor of Pediatrics
Riley Hospital for Children at Indiana University Health
Indiana University School of Medicine
Automotive Safety Program
Section of Developmental Pediatrics
Indianapolis, IN

## Slide 2: Child Occupant Protection
Great Measures of Success

## Slide 3: Persistent Gaps in Child Occupant Protection
Child Passengers on Airplanes
School Bus Transportation
Safe Transportation for Children with Special Needs
Occupant Protection for Ambulance Passengers

## Slide 4: Occupant Protection for Ambulance Passengers
Front occupant protection
Rear compartment attendant protection
Rear compartment patient protection
Special considerations for child occupants

## Slide 5: Incubator Video
AAAM, 1998

## Slide 6: 6 YO w/Cot Restraints

## Slide 8: Convertible CSS: Cot Belt Through RF & FF Belt Path

## Slide 9: Crash Test Video: Convertible

## Slide 10
Test | Dummy Mass (kg) | Head Peak g | HIC | Chest Peak g | Chest g ≥3 ms | Max Angle
Cvt – A | 15 | 41 | 362 | 43 | 42 | 53°
Cvt – B1 | 15 | 48 | 739 | 48 | 48 | 77°
Cvt – B2 | 15 | 52 | 460 | 46 | 45 | 54°
Cvt – B3 | 18 | 52 | 501 | 44 | 43 | 52°
FMVSS 213 | 15 | n/a | 1000 | n/a | 60 | 70°
Acceleration and maximum back-angel results for 3-year dummies in convertible child restraints secured facing rearward with two belts on an ambulance cot, with FMVSS 213 criteria
AAAM, 2001

## Slide 11
Dream Ride Car Bed

## Slide 12: Crash Test Video: Car Bed

## Slide 13
Test | Dummy Mass (kg) | Head Peak g | HIC 22 ms | Chest Peak g | Chest g ≥3 ms
CB – A1 | 8 | 72 | 520 | 68 | 65
CB – A2 | 8 | 52 | 405 | 63 | 55
Melvin, 1995 | 8 | 50 | 390 | 50 | n/a
Acceleration results for 6-month dummies in car beds secured laterally with two belts on an ambulance cot, with Melvin [1995] criteria.
AAAM, 2001

## Slide 14
6 months
61 cm.
7.3 kg.

## Slide 15
6 months
61 cm.
7.3 kg.

## Slide 16
2 years
90 cm.
13.8 kg.

## Slide 17
2 ½ years
98 cm.
15.5 kg.

## Slide 18
5 years
96.6 cm.
16 kg.

## Slide 19
7 years
115.5 cm.
23.4 kg.

## Slide 20
10 years
134.6 cm.
32 kg.

## Slide 21
This seat will be rear facing in the vehicle. In this picture, the seat is not tight enough.

## Slide 24
http://search.usa.gov/search?utf8=%E2%9C%93&affiliate=dot-nhtsa&query=ems+ambulance+working+group

## Slide 25
Recommendations:
  For a child who is uninjured/not ill
  For a child who is ill and/or injured and whose condition does not require continuous and/or intensive medical monitoring and/or interventions
  For a child whose condition requires continuous and/or intensive medical monitoring and/or interventions
  For a child whose condition requires spinal immobilization and/or lying flat
  For a child or children who require transport as part of a multiple patient transport (newborn with mother, multiple children, etc.)
Five Situations were Identified as Most Frequently Faced by EMS Providers & Interfacility Transport Teams
Notes: Straight from the Recommendations – Note Idaho has created a brochure that includes these five situations in one page handout!
See slide at the end

## Slide 26: Improving Occupant Protection for Non-Critical Pediatric Patients in Ambulances: A Training Curriculum for EMS Personnel
EMS Training
NHTSA, NCS, Riley Hospital

## Slide 27: EMS Improving Occupant Protection for Non-critical Patients in Ambulances
Module to train EMS providers on child restraints for ambulance use
Instructed by CPST with EMS certification
Length-4 hours
Available at www.preventinjury.org or 1 800 KID N Car

## Slide 28: Safe Guard Transport by IMMI
  Cot-mounted restraint for patients over 1 year of age from 22 to 100 lbs
Color-coded installation system for ease of use
Restraint weighs 22 pounds
5-point harness system with one-handed adjustment for harness height and tightness
Notes: SafeGuard collaborated with Riley Hospital to develop a new pediatric transport solution which incorporates all of these design recommendations.
The new solution is the first cot-mounted restraint designed to transport pediatric patients of a wide range of sizes from 22 to 100 pounds.

## Slide 29: Safe Guard Transport by IMMI
Children 22-40 pounds can use with cot back angle at 70 and 45 degrees
Children 40-100 pounds can use with cot back angle at 70 degrees and completely flat
Not intended for use with potential spinal cord injuries
Crash test footage available on website www.IMMInet.com 317-896-9531
Notes: First, let’s get a basic understanding how the restraint works:
  Color-coded webbing attaches the restraint to the cot
  A complete 5-point harness with automatic height adjustment secures the child
  And, a wipe-clean foam pad & replaceable webbing facilitate care & cleaning
It is important to note this restraint is NOT intended for use with potential spinal cord injuries.
Next, a brief video will demonstrate installation and use of the restraint.
[Video will play AUTOMATICALLY – no need to click]

## Slide 30
AAP PEPP, 2016
Ambulance-specific child restraint accommodating children 10-40 pounds

## Slide 31: Pedi-Mate by Ferno
For infants and toddlers 10-40 pounds
For use on specific Ferno ambulance cots
3 straps attach to cot
5-point harness system
Made of lightweight vinyl, rolls up for storage
Contact manufacturer for crash test information 1-877-733-0911
www.ferno.com

## Slide 32: EP-96 The Rescu-Air: Air Filled Child Transport Seat
For children 20-40 pounds and less than 40” tall
Stores in 21” x 14” x 6” padded carrying case
Weighs 12 pounds
Must purchase “cot harness system” separately to use on ambulance cot
Notes: Instructions for the “cot harness system” may not be included with straps.

## Slide 33: EP-96 The Rescu-Air: Air Filled Child Transport Seat
Five-point restraint system with pelvic adjustment
2-level adjustable shoulder harness
Inflates/deflates with included 12v DC pump in 60 seconds
Cot installation system sold separately
According to manufacturer meets FMVSS213
Contact manufacturer for crash test information
1-800-322-5725
www.epandr.com

## Slide 35: Simulated Crash Tests of Alternative 5-point Restraint (Infant’s head toward front)
Pretest | Incubator cover begins to detach | Maximum dummy displacement
FMVSS 213 crash
pulse: 48 kph (30 mph)
24 G
Civil Aerospace Medical
Institute (CAMI)
newborn infant dummy
(3.38 kg, 52 cm)
SAE 2009-01-2832

## Slide 38: Kangoofix System
“Certified CEN 1789, 2007-a2010 compliant”
Ferno Norden

## Slide 40: Istanbul, Turkey

## Slide 41: Embrace for Neonates

## Slide 42: Proposed Goals Safe Transport of Children Committee (NASEMSO)
To recommend the criteria or specifications for proper restraint of children in ambulances. Such criteria will be evidence-based and will consider safety of both patients and providers.
To have the recommended criteria adopted by one or more accredited standard setting organizations.
To develop a strategy and resources for educating EMS providers on safely transporting children in ground ambulances based on the recommended criteria or standards.

## Slide 44: Kangoofix In Use Video

## Slide 46
Combined, side impact injuries occurred in 14.6/1000 children and 26.8% of crashes. According to PCPS: Children in belt positioning boosters were at a 58% reduction in risk of injury than those in seat belts in side impact crashes.
Partners for Child Passenger Safety • www.chop.edu/service/car-seat-safety-for-kids/index.html
Annual Proceedings of the Association for the Advancement of Automotive Medicine, 2005.